CSCE 312 Computer Organization	10/11/2015
Gustavo Estrela de Matos	925003559
Problem 1
1 -
2 -
3-

The performance of the algorithms were similar, but it was possible to see that solution 1 was the fastest and the solution 2 was the slowest.

4 – Solution 1 was the fastest because it has the fewest number of conditions and applications of masks. The solution from lab1 has a similar number of conditions, but applies masks more than the solution 1, which probably was the reason this solution was slower than the fastest. Solution 2 was the slowest, probably because it has too many conditions, because in the worst case it can verify all the possible input values.

5 – The problem in my solution is that it applies masks too many times in the input variable. Possible solutions could be changing the way the conditions are verified, to something similar to solution 1, or using variables to keep the result of masks (it wouldn't be a good solution because it would cause waste of memory).

Problem 2
1 – SPST means Single Pole, Single Throw. NO – normally open.

Problem 3
1 – Assuming that actuators are enabled for one device at time we can use the negation of the lines to determine which device is being turned off.

Address bus lines				I/O Enable	Actuator control lines					Comment
A3	A2	A1	A0		A/c	D0	D1	D2	D3	Engine starter	Wipers
X	X	X	X	0	0	0	0	0	0	0	0	Nothing happens
0	0	0	0	0	0	0	0	0	0	0	0	Nothing happens
0	0	0	0	1	1	0	0	0	0	0	0	A/c get turned on
0	0	0	1	1	0	1	0	0	0	0	0	Door 1 gets locked
0	0	1	0	1	0	0	1	0	0	0	0	Door 2 gets locked
0	0	1	1	1	0	0	0	1	0	0	0	Door 3 gets locked
0	1	0	0	1	0	0	0	0	1	0	0	Door 4 gets locked
0	1	0	1	1	0	0	0	0	0	1	0	Engine starts
0	1	1	0	1	0	0	0	0	0	0	1	Wipers turned on
0	1	1	1	1	0	0	0	0	0	0	0	Nothing happens
1	0	0	0	1	0	1	1	1	1	1	1	A/c get turned off
1	0	0	1	1	1	0	1	1	1	1	1	Door 1 unlocked
1	0	1	0	1	1	1	0	1	1	1	1	Door 2 unlocked
1	0	1	1	1	1	1	1	0	1	1	1	Door 3 unlocked
1	1	0	0	1	1	1	1	1	0	1	1	Door 4 unlocked
1	1	0	1	1	1	1	1	1	1	0	1	Engine stops
1	1	1	0	1	1	1	1	1	1	1	0	Wipers turned off
1	1	1	1	1	1	1	1	1	1	1	1	Nothing happens